## Slide 1: Pedestrian Wayfinding for People with Disabilities
Southwestern Pennsylvania Partnership for Aging 2017 Annual Conference
Presented by: NICK SINAGRA, SOFTWARE DEVELOPER, PATHVU

## Slide 2: Agenda
Background
Current Guidelines
pathVu Mission
Problem
Data Collection Tools
Data Visualization
Data Analysis
Partners

## Slide 3: University of Pittsburgh and Human Engineering Research Laboratories

## Slide 4: The Problem
1 in 3 older adults trip and fall each year
Wheelchair users
  Falling out of the wheelchair is leading cause of injury
  Say physical environment limits community participation
  Poorly maintained sidewalks can cause dangerous vibrations
This limits
  Safety
    Trip and fall injuries
    Dangerous vibrations
    Obesity
  Community participation
  Transit ridership
Total cost of this issue is $34 Billion in direct medical bills annually in the U.S.
!
Notes: What we’re looking for here: simple problem statement + clear indication of magnitude. Is this a problem worth investing in? Exact wording of magnitude statement will of course vary – it may be about money, lives, etc.

## Slide 5: ADAAG and PROWAG
Americans with Disabilities Act (ADA) Accessibility Guidelines
Public Rights of Way Accessibility Guidelines (PROWAG)
Access Board governs PROWAG/ADAAG
PROWAG Guidelines
  Curb Ramps
  Access Aisles
  Pedestrian Signals
  Running Slope (5 deg or grade of road)
  Cross Slope (2 deg)
  Level Change (1/4” or 1/2”)
  Width (4 feet)
  Stable, Firm, and Slip Resistant
  Roughness??

## Slide 6: Roughness Standard
Standard Practice for Computing Wheelchair Pathway Roughness Index related to User comfort, acceptance and Whole body vibrations from longitudinal profile measurements
ASTM 3028-16

## Slide 7: pathVu Mission
To build a global database of sidewalk and pedestrian pathway data to improve the accessibility, walkability, and safety of all pedestrians – of all abilities.

## Slide 8: Current Sidewalk Data
Many cities do not have GIS maps of sidewalks/crosswalks
Lack of sidewalk data can make it difficult to prioritize improvements
Current pedestrian navigation methods utilize the road network instead of sidewalk maps

## Slide 9: Sidewalk Map Creation
GIS Software
  ArcGIS
  Google Maps/Earth
  OpenStreetMap

## Slide 10: PathMeT
High resolution data
Output Measurements
  Tripping hazards
  Roughness
  Depressions
  Running slope
  Cross slope
  Images (Every 10 feet)
  GPS location

## Slide 11: PathMeT Data Visualization

## Slide 13: Excel Data

## Slide 14: Sample Report

## Slide 15: pathVu App
Crowdsource sidewalk data
Report
  Type
  Location
  Quality
  Image

## Slide 18: Data Collection
1 . Data Collection is organized by Lively Pittsburgh and pathVu including adaptive training of people with and without disabilities in the use of an iPhone or Android app, following the most travelled pedestrian routes in each neighborhood.

## Slide 19: Feedback
2. Feedback and Analysis from local residents and stakeholders including those with disabilities prioritizes which hazards are most pressing to residents with mobility challenges as shown by the pathVu data.

## Slide 20: Advocacy
3. Advocacy is supported as local stakeholders including those with disabilities are invited into conversation and nurtured in their efforts to promote accessibility and walkability.

## Slide 21: Pedestrian Navigation
FHWA ATTRI Contract
“Development of AccessPath: A pedestrian wayfinding tool tailored towards wheelchair users and individuals with visual impairments”
Product Launch Spring 2018
Initial Pilot in Pittsburgh
Following year: 8 additional cities

## Slide 22: Pedestrian Navigation

## Slide 23: Things You Can Do
Map your sidewalks/pathways using GIS software
Use crowdsourcing tools to collect pathway data in your community
Conduct a Walkability Study
Detailed full community assessment
Build partnerships

## Slide 24: Partners, Customers, and Supporters

## Slide 25: Case Study

## Slide 26: Thank You!
Eric Sinagra, CEO eric.sinagra@pathvu.com
Nick Sinagra, Software Developer nick.sinagra@pathvu.com
www.pathvu.com